Date: 13 Nov 2019 – 20191113

Today, I tested the new CROC test board (“NEW”) which has 2 50-pin connectors to directly connect to BEB. I also did a comparison between the previous board (with the CROC_to_BEB board), which I call “OLD”, and the new one for the RC time constant after the clamp.

Setup:
FPGA→HSMC cable → BEB3 (#1) +external power supply→ NEW / OLD CROC test board

→ FPGA:
no external trigger from the generator is needed
the SMA out will provide trigger to the generator for the input signal that will be used.

→ BEB
# OLD Power supply consumption
+12V → ~0.190 A
-5 V → ~0.022 A
+3.3 V→0.01 A
# NEW Power supply consumption
+12 V → ~0.370 A	This is a real important thing that needs to be noticed.
-5 V → ~0.022 A
+3.3 V → 0.02 A

→ Version 2 software and firmware for all the tests

→ LabView:
* Gain(6-bit) & CF1 are used
* Transparent mode & DSI are used
Offset=120
POL=POLIB=127
NEN, V0 always ON

→ Generator:
Pulse
Frequency = 50kHz
Delay = 10.3μs
Low = 0mV
High = 50mV
Width = 8μs
L 2.50ns, T 2.50ns
Cycle: 1-Cycle
Trig Delay 0.0ns
Slope Positive
* external trigger from the SMAout of the FPGA
Attenuator = 25
Generator_Ch2out → Attenuator in → Attenuator out → directly to CROC in with BNC_to_SMA cable.
→ This should give a signal of ~2.8mV. Yet, when I measure with the oscilloscope I see a signal of ~5.7mV.

Oscilloscope:
light blue → CROC out Channel 0
orange → conversion pulse (width ~720ns)
purple → SMA out from FPGA

TEST #1: RC time constant with only one clamp in TS1
Transparent mode
→ TS1 = 1
→ TS2 = 15 000
→ single conversion for each TS2
→ sampling period = 20.52 μs (SCR03)

OLD board, gain=15 (SCR02) full time decay
NEW board, gain=15 (SCR04) full time decay

There are data with the LabView for gain=15, 63 and CF1 to analyze.
TEST #2: NEW board, input signal, clamp for every TS2
Transparent mode
→ TS1=1
→ TS2=15 000
→ TS2 has 6 conversions
I have added a delay of about 100 μs between TS2 measurements
→ gain=15
images from full decay scale to 2 periods: SCR05, 06, 07, 08

TEST #3: Like test #2 but I have removed the ~100μs delay.
Transparent mode
→ TS1=1
→ TS2 has 6 conversions
→ TS2 period = 20.55 μs
gain=15 → SCR11
gain=63 → SCR12
CF1 → SCR13
@ in gain mode the clamp is visible in the CROC out signal. On the contrary, in CF1 there is nothing.

TEST #4: DSI mode
Gain=35, RC=6

CF1 & input signal →SCR14 : RD goes UP, RU goes UP
Gain & input signal → SCR15: RD goes DOWN, RU goes UP
→ I do not understand why there is this difference

CF1 & no input → SCR16: RD up, RU down
Gain & no input → SCR17: RD down, RU up
→ Again I do not understand why there is difference